## Slide 1
GE HealthCare
RFID Cart Tracking System
Development Plan & IT Requirements
Pristina Mammography Line · Buc Factory, France · 2026
Stage GE Healthcare · RFID Project Intern
PILOT — Phase 1
Pristina Line · 3 RFID Readers
MQTTS · Oracle GLPROD

## Slide 2
Current Situation — Why We Need This
Manual process with no real-time visibility · 5 identified pain points
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
5 PAIN POINTS — CURRENT FLOW
1
No real-time tracking
Supervisor can't see where each cart is at any moment — blind visibility
2
Manual paper labels
Labels printed & attached by hand — risk of loss, error, mix-up
3
Manual Oracle entry
Water Spider manually creates Work Order in Oracle — slow, error-prone
4
No stock exit trace
Parts leave the supermarket with zero automatic record in Oracle
5
No delay alert
A blocked cart triggers no notification — line stops silently
CURRENT FLOW — AS-IS (all manual)
PLAN
Check Excel planning
Water Spider consults Excel job list
ORA
Create Work Order in Oracle
Manual entry in Oracle GLPROD — slow & error-prone
LBL
Print & attach paper label
Label contains: item, WO number, qty, operation
SMK
Pick parts from Supermarket
TRA / TRB / PHCO aisles — manual pick
WAIT
Push cart to Waiting Area
Cart parked near Pristina workstations
POST
Deliver to workstation
Water Spider pushes cart to correct station
DHR
Operator picks label → opens DHR
Reads label to identify job · starts assembly steps

## Slide 3
My Solution — RFID Automatic Tracking
2 tags per cart · 1 reader at SMK/WA boundary · passage readers
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
CONCEPT: Each cart has 2 RFID tags (START on front · END on back) · 1 reader at Supermarket exit = Waiting Area entrance (same physical point) · Passage readers detect cart moving from WA to workstations
ORACLE
AUTO Move Transaction
START tag scanned at SMK exit
→ Oracle WIP transaction triggered automatically
No manual entry by Water Spider
TRACK
Real-Time Position
Passage reader detects cart direction
→ Status: IN TRANSIT or AT WORKSTATION
Supervisor dashboard live
EMPTY
Empty Cart Detection
END tag scanned at passage reader
→ Cart flagged as EMPTY, mission done
Returns to supermarket queue
ALERT
Automatic Alerts
Cart blocked at workstation >30 min
→ eAndon alert triggered automatically
Zero silent line stops
Hardware
2 RFID Tags / cart
(START front · END back)
Reader #1 — SMK/WA
1 reader = SMK exit
= WA entrance (same point)
Passage Readers
Between WA and posts
(not 1 reader per workstation)
Protocol
MQTTS — port 8883
QoS 1 · TLS encrypted
KEY GAINS: Only 2 readers needed per line · Move transaction fully automatic · Cart position deduced from passage reader · END tag = empty cart signal · No manual task for Water Spider

## Slide 4
Development Approach — Prototype Now · Production Later
MQTTS coded from day 1 · when switching to Linux server, code stays 90% identical
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
NOW — PROTOTYPE (Raspberry Pi)
Hardware
Raspberry Pi 4 (80 €)
MQTT Broker
Mosquitto (port 1883, no TLS)
Protocol
paho-mqtt — MQTTS code
Database
SQLite (local file)
Web server
Flask app.run(debug=True, :5000)
Network
Factory WiFi / Ethernet
Oracle
cx_Oracle → GLPROD
Dashboard
Flask HTML template
Monitoring
None (manual check)
→
same
code
PRODUCTION — LINUX SERVER (IT Managed)
Hardware
Linux Server (IT managed)
MQTT Broker
Mosquitto (port 8883, TLS)
Protocol
paho-mqtt · SAME CODE
Database
MySQL HA (Master + Replica)
Web server
Gunicorn + Nginx HTTPS :443
Network
VLAN Manufacturing (isolated)
Oracle
cx_Oracle → GLPROD · SAME
Dashboard
Flask HTML · SAME CODE
Monitoring
Zabbix + watchdog systemd
= IT sets up / configures
= same code, no change

## Slide 5
What IT Needs to Provide — Final Deployment
6 areas of IT responsibility for production-ready industrial deployment
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
01
Linux Server
· Ubuntu 22.04 LTS (or equivalent)
· 8 core / 16 GB RAM / 200 GB SSD
· SSH access for developer
· systemd for Flask auto-restart (watchdog)
02
Network — VLAN Manufacturing
· Dedicated VLAN for all RFID readers
· Firewall: RFID → server port 8883 only
· Server → Oracle GLPROD port 1521
· Static IP for server + DNS entry
03
TLS Certificates (MQTTS)
· CA certificate (ca.crt) for broker
· Server cert (server.crt + server.key)
· Client certs for each RFID reader
· Annual renewal process defined
04
MySQL Database
· MySQL 8.0 installed + configured
· Create database: rfid_buc_factory
· Create user: rfid_user (limited perms)
· HA setup: Master + Replica (recommended)
05
Oracle GLPROD Access
· Oracle credentials for Flask application
· Read access: WIP_DISCRETE_JOBS table
· Write access: WIP Move Transactions
· Network route: server → Oracle :1521
06
Monitoring & Backup
· Zabbix agent (server availability)
· NAS mount for nightly DB backup
· Log rotation policy (90 days)
· Alert contact: who to call if server down

## Slide 6
What I Need From IT — Right Now (Internship Phase)
Minimum required to validate prototype before end of internship
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
NEEDS RIGHT NOW — PROTOTYPE
1
Oracle GLPROD access
cx_Oracle connection from Raspberry Pi
Read: WIP_DISCRETE_JOBS
Write: WIP Move Transactions API
2
Network — port 1521 open
Firewall rule: RPi → Oracle GLPROD port 1521
(only this port needed for the prototype)
3
Raspberry Pi on factory network
Allow RPi on factory network
Static IP or DHCP reservation
So RFID readers can reach it
4
Port 1883 open (MQTT prototype)
RFID readers → RPi on port 1883
(no TLS needed for pilot, just local MQTT)
Everything else (MySQL, TLS, Nginx, VLAN, NAS...) is handled by IT at final deployment — not needed now.
FINAL DEPLOYMENT — IT MANAGES
IT
Linux Server (Ubuntu 22.04 LTS)
IT
MySQL 8.0 — install, configure, HA
IT
VLAN Manufacturing — RFID isolation
IT
Mosquitto MQTTS — port 8883 + TLS certs
IT
TLS certificates — CA + server + client
IT
Nginx reverse proxy — HTTPS :443
IT
Firewall rules — port whitelist per zone
IT
Zabbix monitoring — server uptime alerts
IT
NAS backup — nightly DB backup, 90 days
IT
Oracle network route — server → GLPROD :1521
IT
Power BI Gateway — KPI dashboards

## Slide 7
Deployment Roadmap — 4 Phases
From internship pilot on Raspberry Pi to full factory Azure cloud
GE HealthCare
RFID Pristina — GE HealthCare Buc | Internal Confidential
Phase
1
Internship Pilot
Now — June 2026
Raspberry Pi 4
SQLite database
MQTTS (port 1883)
Pristina line only
3 RFID readers
Oracle GLPROD
Phase
2
All 6 Lines
Q3 2026
Linux Server IT
MySQL replaces SQLite
All 6 production lines
18 RFID readers
Full Oracle prod
Power BI KPIs
Phase
3
MySQL HA + Redis
Q4 2026
MySQL Master + Replica
Redis cache layer
VLAN Manufacturing
MQTTS port 8883 TLS
Nginx HTTPS :443
eAndon alerts live
Phase
4
Azure Cloud
2027
Azure IoT Hub
Azure SQL (cloud DB)
Multi-factory rollout
CI/CD pipeline
Global dashboards
99.99% SLA
YOU ARE HERE